## Slide 1
The Implementation
of
Peak Detectors
Authors: Aviv Azran and Natty Levi
Supervisor: Alex Zviagintsev

## Slide 2
Background – What is a peak detector?
So, what’s the problem? - Naive peak detector implementation
Project definition and goals
Possible solutions and proposed Architectural designs
What has been done
Summary
Agenda

## Slide 3
Peak detectors capture the extreme of the voltage signal at its input.
A positive peak detector captures the most positive point of the input signal and a negative peak detector captures the most negative point of the input signal.
Background

## Slide 4
Background
Ideally the output of the peak detector circuit tracks or follows the input voltage until the extreme point is reached but holds that value as the input decreases. The ideal peak detector performs this function regardless speed of the input signal. The performance of the physical peak detector is limited by the bandwidth of the input signal.
LTC6244 High Speed Peak Detector by Gabino Alonso and Hassan Kelley

## Slide 5
Background
Ideally the output of the peak detector circuit tracks or follows the input voltage until the extreme point is reached but holds that value as the input decreases. The ideal peak detector performs this function regardless speed of the input signal. The performance of the physical peak detector is limited by the bandwidth of the input signal.
LTC6244 High Speed Peak Detector by Gabino Alonso and Hassan Kelley

## Slide 6
Given a rapidly changing AC input signal,
Peak detectors are used to obtain the peak voltage the signal reaches.
Analysis of spectral and mass spectrometer.
Amplitude modulated wave communication.
Sound measuring instruments.
Applications
Background

## Slide 7
Naive Implementation
The abstract idea of following the peaks of some arbitrary input signal might be naively realized in a circuit.
Impedance
“Something” to hold the peak values while no new peak was detected
“Something” to follow the peaks
We’re going to need:

## Slide 8
problem?
Naive Implementation
Resistor
Diode
Capacitor

## Slide 9
Naive Implementation
YES!
More than one actually…

## Slide 10
Naive Implementation
The circuit cannot precisely track the input peak voltage because the diode is not an ideal diode.
Conclusion – Not for small signals detection.
thus, it has a forward voltage, which its value can be observed as the difference between the input and the output voltage.

## Slide 11
is a slow discharge from the hold capacitor through the leakage and the path provided by the following stage. it makes the output peak voltage deviate from the true peak value.
Peak Detector
Major Challenges
- hold capacitor.
- leakage current.
Droop
is the rate in which this phenomenon happens
  It is proportional to the hold capacitor leakage current.
  It depends on the capacitance of the hold capacitor
  the droop rate is calculated from the following equation:
Droop rate

## Slide 12
is the change of voltage, current or any other electrical quantity per unit of time.
the rate of voltage change across the capacitor is defined by the formula:
The higher the slew rate, the better the reactivity of the peak detector.
  In order to increase the speed of the peak detector for tracing a fast input waveform, the capacitance value of the hold capacitor should be reduced.
Peak Detector
Major Challenges
- hold capacitor.
- charge current.
Slew Rate

## Slide 13
Major Challenges
Tradeoff: droop rate - slew rate
Increasing the slew rate by reducing the capacitance value,
Therefore, there is a trade-off between low droop rate and high slew rate in peak detector design.
As so, constructing a general-signal peak detector might be currently out of reach
will cause a larger droop
because of a faster discharge.

## Slide 14
Project definition
And goals
Conduct resaerch in order to understand the operation and properties of the peak detector topology, emphasizing droop and slew rate dependencies.
    Design 3 alternative peak detector architectures
        Perform an Analysis for each architecture
            Compare the analysis results of the different circuits

## Slide 15
Project definition
And goals II
Acquire knowledge on analog circuit design
Encounter common challenges of analog circuit design
If possible, reach a consensus about the architecture which performs best
Define relations between circuit parameters (geometry, capacitance, etc..) and their effects on the circuits performance (bandwidth, slew rate, droop)
Our goals:

## Slide 16
Possible Solutions
1st Solution: Positive peak detector using source follower
 | 1st circuit
Amplifier type | SF Op-Amp
Circuit operation | Capacitor holds the output peak voltage, when Vin < Vpeak and M1 is off
Droop rate control | Droop rate is controlled by capacitance and current source.

## Slide 17
Possible Solutions
2nd Solution: Positive peak detector using current mirror
 | 2nd circuit
Amplifier type | Differential Amplifier (M1-M4) Current mirror (M5-M6) (diode)
Circuit operation | If Vin > Vpeak, the current through M5 and M6 charging the capacitor.
Droop rate control | The droop rate controlled by capacitance values and current source.

## Slide 18
Possible Solutions
3rd Solution: Differential positive peak detector
 | 3rd circuit
Type of amplifier used | Differential version of peak detector using current mirror
Operation of the circuits | Two input signals are fed into the circuit. The single ended output peak voltage is thus the maximum of the two peak voltages.
Droop rate control | controlled by adjusting the values of capacitance and current source.

## Slide 19
Learning the technology
180nm technology
was selected for this project.
We tested the CMOS behaviors in terms of DC, transient and AC analysis.

## Slide 20
Simulation results: NMOS CS Amplifier
Bode Gain plot
Bode Phase plot
Phase Margin: 111.5deg
Gain: 55.42db
Gain Bandwidth: 74MHz
AC analysis

## Slide 21
Transient Analysis
Value | Parameter
2mV | Vin,ptp
1kHz | Frequency
Vout,ptp = 1.12V
Gain = 56
Vout
Vin

## Slide 22
1st circuit Amplifier-Open Loop
Value | Param
15uA | Idc
3.3V | Vdc
1.5V | Vin,p
1.5V | Vin,n
1kHz | Freq.
Vout = 2.45 V
I = 30uA
Power = 97uW
DC Analysis and operating point

## Slide 23
Simulation results Amplifier
Bode Gain plot
Bode Phase plot
Phase Margin: 102.8 deg
Gain: 50.7dB
Gain Bandwidth: 4.9 MHz
AC analysis

## Slide 24
AC analysis- CMRR
Adm
Gain: 50.7dB
Acm
Gain: -49.89dB
CMRR : 98.62dB

## Slide 25
Non-inverting differential amplifier (vin,p>vin,n)
Value | Param
4mV | Vin,p,ptp
1.6mV | Vin,n,ptp
1kHz | Freq
Vout,ptp = 0.77V
Gain = 323
Vout
Vin, p
Vin, n
Transient Analysis

## Slide 26
inverting differential amplifier (vin,p<vin,n)
Vout,ptp = 0.77 V
Gain = 322
Vout
Vin, p
Vin, n
Value | Param
1.6mV | Vin,p,ptp
4mV | Vin,n,ptp
1kHz | Freq
Transient Analysis

## Slide 27
First Circuit Architecture
Challenges Encounter
1 . While we connected VDD to drain terminal of NMOS transistor that place in the output amplifier, the output voltage(Vpeak) reach to VDD and do not stop on vin,max.
2. When we connect current source/resistor at parallel to Vpeak, and the input fall to zero, The charge from output capacitor start to discharge through the current source.

## Slide 28
The ideal 1st circuit
Constant parameters
At this circuit We use an ideal amplifier with
-gain= 80dB
-Vout, min=0V
-Vout,max=3.3V

## Slide 29
Test 1-General Functionality
- This test checks if the functionality of the circuit behave as expected.
The input is Vexp, rises from 0V to 1.75V.
Cout= 20pF.
- The output follows the input and stay at maximum input even the input voltage fall.

## Slide 30
Test 2- Minimum pulse width
That can be detected
- This test checks what the minimum pulse width that the circuit can detects before the input voltage fall.
Cout= 20pF.
We check several width rectangular input( Vpulse) and found that
.

## Slide 31
Test 3- Max frequency that
Can be detected at the first period
- This test checks the maximum
frequency that can be detected at the first period of sinusoidal input
- Test condition:
Cout= 29.764pF
Can be seen that

## Slide 32
Test 4- Droop Rate depending on
output capacitance
- Test condition:
Vpulse Source
-Can see that there is an inverse
correlation between output
Capacitance and DR;
Large capacitance leads to small DR.
-

## Slide 33
Test 5 – Setting minimum output
capacitance depending on derivative
of the output voltage
We decide to set the following condition for the DR:
This condition allows us a lower bound of output capacitance for correct functionality
-Can see that
met the condition

## Slide 34
Test 6 – Exposure of Slew Rate
phenomena
- In this test we want to see the SR effect occurs in the circuit
- Test condition:
Vpulse Source
-Can see that choosing of small capacitance leads to higher SR,
but in Test 5 we get
.
On the opposite side, large capacitance means smaller DR.
Therefore the minimum pulse width must increase, and need to take it into account

## Slide 35
The 1st real circuit
With output current source

## Slide 36
General Functionality
Can be seen that the output follows the input, but it’s starts to fall down immediately after the input fall
The DR is infinite. This is can be good implement for application that DR do not consider
Vin
Vpeak

## Slide 37
The 1st real circuit
Close Loop- DC Analysis
i=39.65uA
Power Dissipation=130.845uW

## Slide 38
AC Analysis
Phase Margin: 70.8 deg
Gain: 46.68 dB
Bode Gain plot
Bode Phase plot
Gain Bandwidth: 3.634 MHz
GBP: 203.589Mhz

## Slide 39
Vin
Vpeak
Test 1-General Functionality
- This test checks if the functionality of the circuit behave as expected.
- The input is Vexp, rises from 0V to 1.75V. Cout= 20pF.
- The output follows the input and stay at maximum input even the input voltage fall.
- The DR derives from leakage current.

## Slide 40
Test 2- Maximum input
Voltage that can be detected
Vin,1
Vin,2
Vin,3
Vpeak,3
Vpeak,2
Vpeak,1
- We get that the maximum
Input that can be detected
by the circuit
is
- Cout=20pF

## Slide 41
Test 3- Minimum pulse width
That can be detected
Vin,1
Vin,2
Vpeak,2
Vpeak,1
- This test checks what the minimum pulse width that the circuit can detects before the input voltage fall.
Cout= 20pF.
We check several width rectangular input( Vpulse) and found that
.

## Slide 42
Test 4- Max frequency that
Can be detected at the first period
Vin,1
Vin,2
Vin,3
- This test checks the maximum
frequency that can be detected at the first period of sinusoidal input
- Test condition:
Cout= 20pF
- Can see that

## Slide 43
Test 5- Max frequency that
Can be detected at steady state
- This test checks the maximum
frequency that can be detected at at steady state
- Test condition:
above condition chosen because at 80mV the circuit can't follow- stays at 1.65V at tenth KHz
- Can see that
- peak founds at the first period so we decide to do one more test to detect the max frequency

## Slide 44
Test 6- Max frequency that
Can be detected at the first period
at high frequency
- This test checks the maximum
frequency that can be detected at at first period at high frequency
- Test condition:
Can see that
Vpeak

## Slide 45
Test 7- Max sinusoidal input with
Damping factor that can be detected
- This test checks the maximum
voltage that can be detected for sinusoidal input with damping factor
- Test condition:
Can see that for this test
The output follows up to
and after stop the following
Vin
Vpeak

## Slide 46
Test 8- founding range capacitance
For Pulse Width=2*min, Pulse Width
Vin
Vpeak
SR
- This test contains several constrain parameter that gives evaluation of choosing output capacitance for pulse width=2*minimum pulse width(Test 3)
Test condition:
Vpulse: ,
=

## Slide 47
Test 9- founding range capacitance
depending on Droop Rate
Vin
Vpeak
DR
- This test is Figure Of Merit of range capacitance depending on DR
Test condition:
Vpulse Source
-Can see that

## Slide 48
2nd Circuit Architecture
Challenges Encounter
Similar to the 1st circuit when we connected VDD to source terminal of PMOS transistor, the output voltage(Vpeak) reached to VDD and do not stop on vin,max.
we try to solve it by connecting current source parallel to output capacitor. This do not solve the entire problem; we got peak of VDD at the start of the operation.
Eventually the source of the PMOS was connected to source of NMOS diode connection such that the NMOS behave like current source.
In addition, we connect the PMOS as diode connection to prevent infinite DR while the input voltage fall bellow the output volatge.

## Slide 49
2nd Circuit Architecture
Challenges Encounter- example
Vin
Vpeak
- We try several output current that can control on the Discharge capacitor
We get always a peak of VDD
at the first of the operation

## Slide 50
The ideal 2nd circuit
Constant parameters
At this circuit we use an ideal amplifier with
-gain= 80dB
-Vout, min=0V
-Vout,max=3.3V

## Slide 51
Comparison between 1st
and 2nd ideal circuit
-We did the same tests in
the 2nd circuit and summarized
The result at Table comparison
- The use of the 1st or 2nd circuit can be considered
dependent on specific application
for example- for high input voltage detection 1st circuit
Is better, but for minimum pulse width 2nd circuit preferred
- The performances of the 1st circuit
are better in more tests but both of
them behave as peak detector

## Slide 52
2nd circuit Amplifier
We choose that amplifier because the large gain in open loop.
Also, this is great opportunity to acquire experience in complex amplifier design
NM4
NM2
PM6
PM8
)≅
)≅
Gain:
)

## Slide 53
DC Analysis and operating point
I,max=30mA
Power Dissipation=99mW
Simulation results Amplifier-Open Loop

## Slide 54
AC analysis
Bode Gain plot
Gain Bandwidth: 81.02 KHz
Gain: 83.363dB
GBP: 72.42Mhz
Bode Phase plot
Phase Margin: 70.885 deg

## Slide 55
AC analysis- CMRR
Adm
Gain: 83.363dB
Acm
Gain: -48.4189dB
CMRR : 131.782dB

## Slide 56
Non-inverting differential amplifier (vin,p>vin,n)
Transient Analysis
Vout
Vin, p
Vin, n
Vout,ptp=0.1725V
Gain=14375

## Slide 57
inverting differential amplifier (vin,p<vin,n)
Transient Analysis
Vout
Vin, p
Vin, n
Vout,ptp=0.17292V
Gain=14410

## Slide 58
The 2nd real circuit
Close Loop- DC Analysis
I=30mA
Power Dissipation=99.05mW

## Slide 59
AC Analysis
Phase Margin: 170.2 deg
Bode Phase plot
Bode Gain plot
DC Gain: 88.0436 mdB
Gain@high frequency:
46.4437 dB

## Slide 60
Comparison between 1st
and 2nd real circuit
The performance of the 1st circuit is better in more tests, but both of them behave as peak detector.
The usage depends on application. for ex. :
  detection of higher frequency at first peak - 1st (Test 4),
  detection higher frequency at Steady State- 2nd

## Slide 61
3rd architecture with
real amplifier

## Slide 62
Test- Tracing of 2 sinusoidal
Input with different amplitude
- Test Purpose- given 2 sinusoidal input , we’d like to check the tracing operation:
our assumption is that the output will follow the larger amplitude out of 2 inputs.
-Test condition:
the result is as we expected, see that the output
voltage stop tracing of right input and starts tracing
after left input

## Slide 63
Tracing of 2 sinusoidal
Input with different amplitude-
continue
-Can see that the transition of tracing
from the right input to the left input
occurs at 1.809Sec

## Slide 64
Designing amplifiers in open/close loop- amp equation,
stability at operating point, DC, ac and transient analysis, implementation equation transistors and optimization of geometrical size transistors inside the circuit
Problems solving- building abilities to deal with challenges during designing circuit , by means of thinking and analyzing goal-oriented
Independent work- we try to work independent during the project, but it was important for us to get instruction from Alex, our guidance, when we were need him. This process helps us to develop accountability and initiative. Also, during the project we added more test in order to produce theoretical and practical experiences
Summary- What do we learn

## Slide 65
Software learning- we learn Virtuoso and part of the tools it provide for circuits design
Prior planning- early preparation of goals project in theoretical part minimize the problem during the design.
previous experience helps
Complexity of circuits designing- Complex circuits; more transistors and tight restriction, require higher skill
Interesting Domain- designing of analog circuits in general and peak detectors in particular, putting challenges and restrictions that solving them gives great satisfaction. Also, the circuits have great importance in engineering application such as medical equipment, sound, computer, etc.
What do we learn- continue
Thank you